SECTION (40 9510) (13320)

CONTROL AND DATA NETWORK EQUIPMENT

# GENERAL

# PRODUCTS

## COPPER TERMINATION PATCH PANELS

### Compact Shielded CAT 6 Patch Panel

#### Compact Shielded CAT 6 Patch Panel shall consist of a din-rail or surface mount housing with an integrated faceplate, housing up to twelve shielded CAT 6 jacks. Keystone jacks shall be backwards compatible with CAT 5 cabling.

#### Mounting – Compact Shielded CAT 6 Patch Panel shall able to be din-rail or surface mounted.  Mounting options shall include, at a minimum, rear din-rail mount, side din-rail mount and rear surface mount.

#### Mechanical Construction – Compact Shielded CAT 6 Patch Panel enclosure and faceplate shall be constructed of 18 gauge steel and powder coat painted to provide metal corrosion protection.

#### Dimensions – Compact Shielded CAT 6 Patch Panel dimensions, with mounting, cable glands and fiber optic adapter hardware installed, shall be no larger than a height of 5.5 inches, a depth of 5.33 inches and a width of 3.68 inches.

#### Approvals – Compact Shielded CAT 6 Patch Panel shall be UL Listed 1863.

#### Faceplate slide-out mechanism – Compact Shielded CAT 6 Patch Panel shall include a mechanism to support the faceplate while it is opened, permitting access to the CAT 6 jacks on the rear of the faceplate without the technician holding the faceplate itself.

#### Compact Fiber Optic Patch panel shall be SNAP Cu series as manufactured by DINSpace or Approved Equal.

# EXECUTION		N/A

END OF SECTION