SECTION (40 9510) (13320)

CONTROL AND DATA NETWORK EQUIPMENT

# PRODUCTS

## 19” RACKMOUNT DIN-RAIL ADAPTER WITH CABLE MANAGEMENT BRACKET

### Provide a 19” Rackmount DIN-Rail Adapter with cable management as shown in the Drawings and specified herein.

### Unit shall consist of a powder-coat painted one-piece 16 gauge steel body with 35mm DIN-Rail installed across the interior width.

### The Adapter panel shall be able to support up to 50 pounds of mounted equipment and require no more than 5U of rack space.

### The DIN-Rail Adapter shall have four preinstalled cable hangers and cabling pass-through ports on each side.

### 19” Rackmount DIN-Rail Adapter with cable management shall be BRKT-19DR-5U-CM as manufactured by DINSpace or Approved Equal.

## 19” RACKMOUNT DIN-RAIL ADAPTER

### Provide a 19” Rackmount DIN-Rail Adapter as shown in the Drawings and specified herein.

### Unit shall consist of a powder-coat painted one-piece 16 gauge steel body with a single 35mm DIN-Rail installed across the interior width.

### The Adapter panel shall be able to support up to 50 pounds of mounted equipment and require no more than 4U of rack space.

### The DIN-Rail Adapter shall cabling pass-through ports on each side.

### 19” Rackmount DIN-Rail Adapter shall be BRKT-19DR-4U as manufactured by DINSpace or Approved Equal.