SECTION (40 9533) (13321)

FIBER OPTIC CABLING AND EQUIPMENT

# GENERAL

# PRODUCTS

## FIBER OPTIC TERMINATION PATCH PANELS

### Compact Fiber Optic Patch Panel

#### Compact Fiber Optic Patch panel shall consist of a din-rail or surface mount housing with an integrated faceplate, housing up to twelve fiber optic patch adapters.

#### Mounting – Compact Fiber Optic Patch panel shall able to be din-rail or surface mounted.  Mounting options shall include, at a minimum, rear din-rail mount, side din-rail mount and rear surface mount.

#### Mechanical Construction – Compact Fiber Optic Patch panel enclosure and faceplate shall be constructed of 18 gauge steel and powder coat painted to provide metal corrosion protection.

#### Dimensions – Compact Fiber Optic Patch panel dimensions, with mounting, cable glands and fiber optic adapter hardware installed, shall be no larger than a height of 7.75 inches, a depth of 5.75 inches and a width of 3.5 inches.

#### Approvals – Compact Fiber Optic Patch panel shall be UL Listed 1863.

#### Faceplate slide-out mechanism – Compact Fiber Optic Patch panel shall include a mechanism to support the  faceplate while it is opened, permitting access to the fiber optic adapter connections on the rear of the faceplate without the technician holding the faceplate itself.

#### Support for fusion splices - Compact Patch panel shall provide an integrated fusion splice alignment and protection fixture to protect and secure fusion splice joints.

#### Compact Fiber Optic Patch panel shall be SNAP and/or SNAPXL series as manufactured by DINSpace or Approved Equal.

# EXECUTION		N/A

END OF SECTION